## Slide 1: CheMin
Group-2
Poonam Lakhangaonkar
Hiren Patel
Valentin BERTHOMIER
Rajnish Kumar

## Slide 2: Introduction
CheMin is a mineralogy instrument that will identify and quantify the minerals present in rocks and soil powder samples delivered by the rover's robotic arm

## Slide 3: Description
CheMin Instrument is located inside the main body of the rover
CheMin Uses
  A technique called X-ray diffraction (XRD) for mineralogy characterization
  X-ray fluorescence (XRF) for elemental characterization
  A single detector for both measurements
  One moving part (Sample wheel)

## Slide 4
(CheMin XRD/XRF instrument )

## Slide 5: What CheMin does?
CheMin analyze the sample delivered to it by SA/SPaH
It identifies the minerals present in Mars soil & rocks
Mineralogy helps CheMin to assess the involvement of water in their formation, position and alteration
CheMin data is useful in the search for potential mineral energy sources for life or indicators for past habitable environments

## Slide 6: CheMin Requirements
Power Requirements
  Chemin require 250W-hr power per evening for processing.
  CheMin is limited to approximately 4 hours of analysis per evening of operation, with the remaining energy allocated for pre-analysis warm-up of the X-ray source, and post-analysis data processing and transfer.
  The complete analysis of any one sample can take up to 10 hours, thus requiring multiple evenings to analyze a sample.

## Slide 7: CheMin components
Funnel
  Receives drill powders or scoop samples from the SA/SPaH system
  Maximum of 65 mm3 of sample material is delivered
  It contains a 1-mm mesh screen to keep larger than expected grains from entering the CheMin sample handling system
  Grains that pass through the screen will pass into the upper reservoir portion of the sample cell
  CheMin may reduce contamination by sample dilution

## Slide 8: CheMin components
Sample cell and sample wheel
  Carries 27 reusable sample cells and 5 permanent reference standards
  Only 10 mm^3 material is required to fill the sample cell
  Remaining sample goes to reservoir (which is above cell)
  During filling, analysis, and dumping, the sample cell is shaken by piezoelectric actuators (piezos)

## Slide 9: (Sample Wheel And Sample cell)

## Slide 10: CheMin components
X-Ray Beam
  X-ray beam from the X-ray tube is directed through a transmission sample cell containing sample
  X-ray sensitive CCD imager is positioned on the opposite side of the sample from the source
  X-ray diffraction occurs with the crystal material and form the rings i.e. a two-dimensional image that constitutes the diffraction pattern

## Slide 11: CheMin Process
CONFIG PHASE
  Position the X-ray sensitive CDD imager
  Receive drilled powder through the drill, scoop and CHIMRA sorting assembly

## Slide 12: CheMin Process
FILLING PHASE
  Open chemin inlet protection cover
  16 dual cells on the sample wheel -> 1piezzo for each dual cell
  piezzo is active during filling analysis and dumping
  Turn on piezzoelectric actuators number X
  put sample in the funnel
  Close inlet protection cover
  If received sample contains more than 5% of contamination then sample rejected

## Slide 13: CheMin Process
ANALYSIS PHASE
  Turn on X-ray beam
  CDD reads out and erase the X-ray flux multiple times (+1000times) for analysis
  Data handling
  Identify energy of X-rays strikes by the detector and produce 2D image of diffraction pattern
  Sum all the X-ray detected by CDD into a histogram of number of photon Vs photon NRJ
  Sum the 2D pattern circumferentially about the central non-diffracted beam to create a 1D 2theta plot

## Slide 14: CheMin Process
DUMPING PHASE
  Rotate the sample wheel 1800 (sample cell inversion)
  Empty the cell after use by inverting and vibrating the sample cell over the sump
  Rotate back to the next sample slot
  Rotate the sample wheel 1800-X (X corresponds to the distance between sample cells)
  Turn off piezzo

## Slide 15: CheMin Commands
chemin on: start the chemin process
xray_set_ position:set the xray position towards sample
sample_receive:this message from telecommunication module
cell _next:from the sample
cell_clean_current:dump the sample
inlet_open:open the
inlet_close:

## Slide 16: CheMin Commands
xray_turn_on: turn on the x-ray beam
analysis_start:start analysis on sample
cdd_create_diffreaction_image:
cdd_create_1d_2t_plot:
send_result:send result to telecommunication server
power_off:turn off the chemin and terminate the process.

## Slide 17: Code Explanation
SimulateRoverMain
  Module creation
    CheMinModuleMain
    Power Server
    Telecom Server
  Module launching
    CheMinModuleMain is launched
      Threads for CheMin server and CheMin process are created & started
    Server threads for Power and Telecom are created & started

## Slide 18: Code Explanation
CheMin server
  If message is ‘chemin_on’
    Set CCU to true and create CheminClient(9013->power) thread and start it
  If message is ‘power on’
    Launch chemin process create CheminClient(9002->Telecom) thread and start it
  If message is ‘Power Off’
    Then free Chemin threads

## Slide 19: Code Explanation
CheMin Client
  If port is 9013
    PowerRequirement is sent to PowerClient
  If port is 9002
    XrdDiffraction image is sent to TelecomClient

## Slide 20: Code Explanation
CheMin Process - can receive the text file which contains the commands to execute
  f_xray_set_position()
    set and configure x-ray beam position
  f_sample_receive()
    launch the powder sample receiving procedure
    If inlet cover is opened, abort the operation

## Slide 21: Code Explanation
  f_cell_go_to(5)
    Choose the sample cell (depending on given sample cell number and current sample cell)
  f_cell_clean_current()
    Start the cleaning procedure
  f_inlet_open()
    Open inlet cover if not opened already

## Slide 22: Code Explanation
  f_piezzo_tun_on(v_current_sample_cell/2)
    Turn on the given piezzo if not on
  f_inlet_close()
    Close inlet cover if not closed already
  f_piezzo_turn_off(v_current_sample_cell/2)
    Turn off the given piezzo if not off
  f_xray_turn_on()
    Turn x-ray on

## Slide 23: Code Explanation
  f_analysis_start()
    Verify that every component is ready to start analysis phase
      X-ray position
      X-ray on
      Inlet cover closed
      Sample cell contamination checked
      Sample not contaminated
    If all above checks satisfied then turn off piezzo

## Slide 24: Code Explanation
  f_analysis_start()
    Starts analysis
      play music ‘voice.mp3’
      f_cdd_read_erase()

## Slide 25: Code Explanation
  f_cdd_create_diffraction_image()
    Create diffraction image
  f_cdd_create_1d_2t_plot()
    Create 1D 2theta plot image
  f_send_results()
    End of process, send results to telecom

## Slide 26: Code Explanation
Power Server
  Waits for client message
  If receive message, print it
    then create power client(9008->CheminServer) thread and start it

## Slide 27: Code Explanation
Power Client
  Print socket port
  If socket port is 9008
    then send "POWER ON" to port 9008 (to Chemin Server)

## Slide 28: Code Explanation
Telecom Server
  Waits for client message
  If receive message print it
    then create telecom client(9008->CheminServer) thread and start it

## Slide 29: Code Explanation
Telecom Client
  Print socket port
  If socket port is 9008
    then send "Chemin receives telecom acknowledge" to port 9008 (to Chemin Server)